## Slide 1
Validating sensors in self-driving cars
Jonathan Ahlstedt /2020-10-30

## Slide 2: Validating sensors in self-driving cars
Company and team introduction
System setup
Object tracking
Lane detection
A day at work
Features in development
2020-10-30
Ground Truth systems and tools

## Slide 3: Same team, three different companies
~120 employees
~60 employees + Money
~700 employees
~500 employees
Sweden office
Us + Germany office

## Slide 5: The Team
2020-10-30
Ground Truth systems and tools

## Slide 6: The Team
2020-10-30
Ground Truth systems and tools

## Slide 7: So we built an autonomous vehicle – What now?
2020-10-30
Ground Truth systems and tools
How do we sell it?
Legal aspects
  We have to make sure our product abides by current and future laws set by legislators around the world.
Public opinion
  How do we make people ride the cars when an error might be fatal?
We have to prove to the world that our vehicles are safe!
Vienna Convention Article 8
Every moving vehicle OR COMBINATION OF VEHICLES SHALL HAVE A DRIVER.
Every driver shall at all timesbe able to control his vehicle or guide his animals.
Participation in the Vienna Convention

## Slide 8: Previous experience tells us that
2020-10-30
Ground Truth systems and tools
Functional Safety depends heavily on sensor performance
Specification from sensor suppliers reflects performance but is usually not objectively true
  Suppliers might overpromise
  Suppliers might not know the statistical performance of their sensors
Sensors that are to be used are sometimes not completed. Thus, no-one knows the true performance of the finished product
So how do you measure sensor accuracy?
Simple! Compare sensor output to a reference

## Slide 9: Our solution – Ground Truth Roofbox
2020-10-30
Ground Truth systems and tools
Video introduction

## Slide 10: Use cases and features
2020-10-30
Ground Truth systems and tools
Camera FOV
Lidar FOV
Reference sensor data is needed in real traffic for Zenuity to:
  Reduce manual verification
  Extend test-track verification to real-world
  Automate verification
  Perform statistical verification
The system provides 360 degree reference data of the environment of the vehicle and is easy to use
Collected data is automatically post processed offline, documented and formatted for use in verification and development
Inhouse-developed Roofbox and Software includes
  Lidar (range ~200 m)
  Cameras
  GPS/IMU
Sensors can be replaced or added to follow state-of-the art technologies

## Slide 11: Object tracking – step by step
2020-10-30
Ground Truth systems and tools
Raw pointcloud
Ground removal
Object segmentation
On road filtering
128 + 16 + 16 Lasers
10Hz rotations
~260000 points per rotation
X,Y,Z,Intensity
Adaptive progressive morphological filtering
Spherical conditional Euclidian clustering
Grid based greedy search for planar grids

## Slide 12: Object tracking – step by step
2020-10-30
Ground Truth systems and tools
Initial classification
Tracking and post-classification
Support vector machine
  LibSVM
  Single-frame
  Geometry-based
Independent Forward and backward pass Kalman filter
Merge tracklets
Re-filter
Rauch-Tung-Striebel smoothing
Association based on weighted distance, classes, lifetime and other attributes
Post-classification to find most probable class during object lifetime

## Slide 13: Lane detection – step by step
2020-10-30
Ground Truth systems and tools
Lane marking detection
Lane marker tracking
Find lane marking points by looking at intensity
Track the center of lane markings to filter out connected lane marking segments
Lane detection
Use tracked lane centers to find where lanes are
Camera fusion
Find lanes using high reflectivity points in camera

## Slide 14: One day at work
2020-10-30
Ground Truth systems and tools
Get to office at 8.00
  Review others code
  Answer emails
  Do some small patch
  Check in with other teams
Standup at 10.00
  Does someone need help?
  Any blockers?
  What will you work with today?
80% of team does lunch training 10.15-11.00
  Gym (Monday/Wednesday)
  Running (Tuesday/Thursday)
Lunch 11-12
Work 12-14
  Develop new feature
  Attend a meeting with another team
Team gets some air (and fika) 14-14.30
14.30-17~ Continue coding until I leave
– Corona edition
Working from home
  Everyday 9-18
  Never really leave the safety of my home
Extra online sync meetings
Small online sessions when working on the same feature freature with others.
All in all work is not affected, and it owkrs out pretty well! =)

## Slide 16: Bonus info – Camera object detection
2020-10-30
Ground Truth systems and tools
Tested running an open-source “Faster R-CNN Mask"
Trained on the COCO dataset.
Latest version – Almost integrated in toolchain

## Slide 17: Global/Local positioning GT
2020-10-30
Ground Truth systems and tools
OXTS RT3003
GPS and IMU data is fused with base station information
Result: 1cm globally accurate position